|  | BEFORE HAUL OUT: Top off Diesel Tank before hauling- add fuel stabilizer & Biocide Pump seawater through heads overboard- clean out all lines Remove Sails Remove all Soda- diet/w/o sugar will freeze & explode Remove all spare propane bottles (Grill) PULL SPEED SENSOR- or it will be crushed by the travel lift! RV Antifreeze- Used 12 gallons winter 2021 |
| --- | --- |
|  | ENGINE (2 gal) Change Engine Oil & Filter (while hot) Cap 6-7 Quarts Hoses Change Transmission Fluid Cap ~1.5 Quarts Dextron III Mercon Don’t screw in dipstick to read level, use paper towel to read level. Change Fuel Filters Engine (every 2 years: 2015/2017) Drain water from Racor Filter Air intake- clean Pull Strainer on raw water Strainer & Clean, Vacuum out water Check: Belts, Hoses, Motor Mounts Pull Raw Water impeller **REPLACED SPRING 2021** Pull Raw Water Intake- Flush with 2 Gal of Glycol Antifreeze Check exhaust Leave disconnected until finished with A/C system Blow out seacock with air while opening/closing Drain Seacock (remove plug) Plug Exhaust port (transom) with Rag batteries- Charge and Then Disconnect |
|  | Water Tanks (4 Gal ALL without engine) Drain Fwd, Port and Stbd tanks using 12v pump. Vacuum out Port and Stbd Tanks to remove remaining water. Remove fresh water strainer & cover- Apply shop vac here and open up P&S & FWD tank lines to remove all water in the lines between the tanks and the manifold. Use Air Compressor to blow out water in lines/plug in adapter/bypass pump Use air to empty water heater- open drain on aft end of Water Heater use pex/hose to galley sink. Blow out remaining water while red bypass valve is open. Put Hot Water Heater line into bypass mode. Clean strainers for Fresh water and sump Close Port & Stbd valves, open Center valve for Forward tank. Using the deck fill, fill forward water tank with 4 Gallons of antifreeze. Unplug Water Heater, Plug in Engine Room Heater Switch water pump on and Run water to Aft Head and Shower until Pink, Fwd Head until Pink Galley sink until Pink Let some into the water heater (via bypass valves) |
|  | A/C Unit (3/4 gal) Option 1 NEW 2015 (could not get to work fall 2017) Pull cap off “T” under Nav Station Use ¾” hose to blow water out of pump/strainer/seacock Close seacock and blow water out of A/C Unit May not have to use antifreeze in A/C Unit. Option 2 (used fall 2021) Pull A/C Coolant Hose Put Funnel into hose and Run Pump to circulate Antifreeze (3/4 gal) Leave running & pull and clean the strainer Blow out seacock with air while opening/closing valve Reconnect the hose and then turn off the AC unit. (Do this QUICKLY). |
|  | Fwd Seacock intake to Washdown Pump (1/2 gal) Pull hose & Run Washdown Pump until pink. (1/2 gal) Clean strainer in fwd anchor locker. Blow out seacock with air while opening/closing valve- leave closed. 5/8” Drain Seacock (remove plug) |
|  | Fwd Head- (2 gal) Turn Diverter valve to Overboard (~1 ½ gal) Pump fast until air comes out of seacock (open and close seacock quickly to get all water out of seacock). Note: If this works then you only need 1 GAL. If not two. Put ½ gal Antifreeze into bowl and pump overboard w/air Drain Seacock (remove plug) make sure you see red antifreeze Turn Diverter valve to TANK (~ ½ Gal) Put funnel into water intake on head (remove plug) Pump (½- 1 gal?) Antifreeze thru head into holding tank. |
|  | Aft Head- (1-2 Gal) Turn Diverter valve to TANK (normal position) Put funnel into raw water intake for head. Pump (1 gal) Antifreeze thru head into holding tank. Blow out raw water intake for head with hose/mouth. Remove seacock drains for intake and overboard. ONLY IF DIVERTER WAS SET TO OVERBOARD THAT SEASON: Turn Diverter valve to Overboard Pump fast until air comes out of seacock (open and close seacock quickly to get all water out of seacock). Put 1 gal Antifreeze into bowl and pump overboard w/air Drain Seacock (remove plug) make sure you see red antifreeze Drain raw water intake Seacock (remove plug) Refrigerator Drain Antifreeze into Refrigerator Drain (Use Antifreeze from Galley Sink) |
|  | Galley Sink Metal tape on port side cockpit drain to plug drain. Disconnect Engine room bilge pump hose & plug opening Rag & Shop vac on sink drain, blow air into seacock under sink and open and close port cockpit drain a few times to remove water. Leave port cockpit seacock closed Cycle seacock under sink to ensure it is drained Remove fuse for Aft bilge pump & reconnect drain line. Misc Cockpit Drain Seacocks in Engine room- Exercise and leave starboard seacock open. Port seacock stays closed (to sink/engine bilgepump) Remove Bimini & Tie up supports Pull engine hoist and install plug on top Remove davits, leave in cockpit Wash down Deck & boat- check for any leaks – ports/etc Winter Cover- Install & Tie Lines OUTSIDE cover to keep it from inflating Re-Energize moisture absorbent pouches |
|  | If Pulling the Mast Remove Windex & Wind Instruments at masthead, Remove VHF Antenna Disconnect all electrical connections at mast step. |

|  | BEFORE HAUL OUT LOAD ON BOAT: Shop Vac, Hoses, Connector, Extra Filter 300’ garden hose & nozzle to wash down boat 100’ extension cord ladder & lock (chain) Anti-freeze bottles oil changer pump oil container for old oil oil for oil change & filters winter cover and supports (PVC Tubing and wood base) rug to cushion boat in slings Blower to clean off Decks Tool Pouch w/hammer, large punch to remove centerboard 4’ plastic Level (Attach to rudder to level boat) |
| --- | --- |

|  | Parts Needed for Winterization: |
| --- | --- |
|  | Fuel Filters (Yanmar P/N 129470-55701 & Racor p/n 2010SM) |
|  | Oil Filter (Yanmar p/n 129150-35150) |
|  | 2 Qts ATF Dextron III Mercon |
|  | 2.0 Gal 15w-40W Oil |
|  | 12 Gal Glycol Antifreeze (Non-Toxic) used 12 gal 2014 |
|  | Fuel Stabilizer |

|  | Spring Cleanup: |
| --- | --- |
|  | Grease Max Prop & Install new Zinc on prop and two 1 ¼” Zinc’s on the shaft |
|  | Spray Antifoulant on Prop |
|  | Paint Bottom Ablative (1 gal just covers) 2007- three Gals gave two coats |
|  | Three gallons of Micron Extra gave two coats & to centerboard w/ ½ gal left |
|  | Used ¼” Nap roller for boat. 9x6 Green Scrub Pads to wet sand hull |
|  | Wax Boat |
|  | Bring to Boat before launching: |
|  | 6 Rug strips for travellift (Oak Harbor has good pads) |
|  | Davits (attic garage) |
|  | Dink |
|  | Sails |
|  | GPS, Binoculars – any electronics taken off the boat for the winter |
|  | Prep for Launch: |
|  | Reconnect Batteries |
|  | Remove Plug Exhaust port (transom) Rag |
|  | Check Transmission Fluid Cap ~1.5 Quarts Dextron III Mercon |
|  | Check Engine Coolant |
|  | Check Engine Oil |
|  | Check Raw Water Impeller (replace/reinstall) replace spring 2015 |
|  | Clean Raw Water Strainer washdown pump |
|  | Check Belt Tension Alternator/Water Pump |
|  | Check Stuffing Box/ PSS Shaft Seal for wear |
|  | Spare Propane back to boat (Grill) |
|  | Cushions Back to boat |
|  | Sails on board |
|  | GPS / Binoculars / VHF / Charts |
|  | Dive Gear back on board |
|  | Just before launch: |
|  | Pull Backstay for TravelLift (Not Necessary at Oak Harbor) |
|  | Dink on davits |
|  | Crank up Centerboard |
|  | Close all seacocks |
|  | . |
|  | After Launch: |
|  | Burp PSS Shaft Seal (get air out) |
|  | Flush Water tanks |
|  | Replace water filter |
|  | Hose out Bilge and Flush |
|  | Light lubrication on Turnbuckles |
|  | Check Rigging Tension |